CRM – Presentation
César DE OLIVEIRA
iCDG Telephony FT
1st August 2016 – draft 0.07

---
CRM Presentation – agenda
CRM Presentation – agenda
CRM Presentation
  - Design overview
    - Architecture
    - MSCs
    - FSMs
    - Threading model
  - Firmware upgrade
  - Source code
  - Debug
    - Logging
    - Test apps
  - TCS2

---
CRM Presentation
CRM Presentation

---
CRM - presentation
CRM - presentation
CRM stands for “Connectivity Resource Manager”
CRM purpose
- Starts/stops/resets the modem according to client needs (resource handling)
- Handling modem FW update and modem customization.
- Notifies modem state to its clients (UP, DOWN, OOS)
- Handles modem crashes
- Synchronizes the startup of modem clients with modem readiness for communication including RPC daemon readiness.
CRM capacity
- Supports several types of modems
- Runs on linux-based OS

---
CRM - presentation
CRM - presentation

---
Design overview
Design overview
Architecture

---
CRM – design overview
CRM – design overview
MODULARITY
CRM is composed of plugins
Loaded at runtime
New platform = a sub-set of new plugins only
COMMUNICATION between modules
Asynchronous function calls
Functions shall be non blocking
RPC like: result of previous request MUST be received before sending a new request

---
CRM – design overview
CRM – design overview
PURPOSE
Handles communication with clients
Registration
Requests
Events
Virtual client
Combines multiple client requests as if Control has a single client
TECHNICAL DETAILS
FSM
Thread
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Loads all plugins
Decision maker according to all events received from the modules
TECHNICAL DETAILS
FSM
Thread
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Detects control deadlocks: PING/PONG
Time keeper during transitions
TECHNICAL DETAILS
Thread
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Bridge between C and Android Java world
Used to
Acquire/release wakelocks
Broadcats intents (platform reboot, telephony event notifier)
TECHNICAL DETAILS
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Selects the firmware to flash
Provides a list of TLV if customization is needed
TECHNICAL DETAILS
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Defines the recovery strategy (warm, cold reset, platform reboot, modem out of service)
TECHNICAL DETAILS
Generic plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Reads modem core dump and stores it in file system
TECHNICAL DETAILS
Thread or Thread+Process
Platform specific plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Customizes the modem on the fly by sending TLV files content
TECHNICAL DETAILS
Thread
Platform specific plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Packages the modem firmware
Uploads the modem firmware
TECHNICAL DETAILS
Thread or Thread+Process
Platform specific plugin

---
CRM – design overview
CRM – design overview
PURPOSE
Abstracts IPC and physical control of the modem
Notifies modem state to control according to HW events
Controls the NVM server
Controls the RPC daemon
TECHNICAL DETAILS
FSM
Threads
Platform specific plugin
SPECIFICITIES
No success/failure request verdict
A request can be sent without waiting for the result of the previous one
Notification is event based
MDM_BUSY is always followed by a second event providing the reason (OFF, DUMP, FLASHING, UNRECOVERRABLE)

---
CRM – design overview
CRM – design overview
PURPOSE
Controls the NVM server, used to sync NVM data in filesystem
TECHNICAL DETAILS
Thread + process
Platform specific plugin

---
Design overview
Design overview
Threading model

---
CRM – threading model
CRM – threading model

---
Design overview
Design overview
MSCs : some use cases

---
CRM – design overview
CRM – design overview
CLA state
Control state
MSC: modem power on sequence
        with firmware upgrade

---
CRM – design overview
CRM – design overview
MSC: AP reset

---
CRM – design overview
CRM – design overview
MSC: core dump

---
Design overview
Design overview
FSMs: some examples

---
CRM – design overview
CRM – design overview
FSM: Control
FSM: Client Abstraction (CLA)

---
CRM – design overview
CRM – design overview
FSM: HAL PCIE
FSM: HAL SoFIA

---
Firmware upgrade
Firmware upgrade

---
CRM - Firmware upgrade
CRM - Firmware upgrade

---
CRM - Firmware upgrade
CRM - Firmware upgrade

---
Source code
Source code
Code organization

---
CRM – source code
CRM – source code
CRM source code is split in different folders:
inc
  - plugins: contains the headers of all plugins
  - utils: contains the headers of CRM utils library. This library contains all shared code (file access, properties, logging, plugins, fsm, thread, etc).
  - test: contains the headers used by unit test apps
- libs: contains the source code of several shared libraries used by CRM (utils, wakelock, test host)
- plugins: contains the source code of all plugins
- main: main of CRM
- mdmcli: CRM implementation of the client library
For each plugin, there is one folder per implementation and for each implementation, there is three folders (implementation, unit test and xml).

---
Debug
Debug

---
CRM – logging
CRM – logging
CRM initialization
Component name
Function name
Name of the plugin to load
Plugin name
Line number
Name of the implementation
Instance id
FSM logging
Name of the FSM
New state
entrance
Event received
Current state
exit
Operation performed
(entry point of a plugin)
Callback
(providing the result of a request)

---
CRM – testing
CRM – testing
3 kind of test applications
Plugin unit test
  - Each plugin is tested with a unit test (Host or/and Target)
  - Used to verify plugin behavior
- Host test: crm_test_host
  - Starts
    - CRM
    - Fake modem (controlled by the test app)
    - Fake client (controlled by the test app)
  - Used to
    - Verify CRM behavior with defined scenarios
    - Easily reproduce error use cases (modem crash, etc)
Target test: crm_test
  - Starts CRM in sanity mode (only the test app is able to register)
  - Used to
    - Catch a regression before patch integration
    - All classic UC are run by this test app
      - Registration
      - Resource handling
      - APIMR
      - Self reset
      - Core dump
      - Full escalation recovery
      - etc

---
Libtcs2
Libtcs2

---
Libtcs2 – API and XML files
Libtcs2 – API and XML files
New API
New XMLs
 no backward compatibility
Usage example:
tcs_init() detects the platform and loads
needed XML files

---
libtcs2 – XML files for streamline
libtcs2 – XML files for streamline
Examples of overlay
List of TLV is appended to original one
List of TLV overwrites the original one
NB: append is the default behavior. Could be omitted
File: Hardware configuration file (ex: TCS_XMM7360_CONF1.xml)
Repo location: device/intel/common/telephony-config/hw_config/
Target location: /system/vendor/etc/telephony/tcs/config/
File: streamline_SF_LTE_CONF_1.xml
Repo location: device/intel/common/telephony-config/streamline/xmls/
Target location: /system/vendor/etc/telephony/tcs/streamline/
Repo location: device/intel/common/telephony-config/catalog/XXX/streamline/
Target location: /system/vendor/etc/telephony/catalog/XXX/streamline/
Name of XML file storing list of TLV files
Mandatory field used by CRM
Name of TLV file